## Slide 1: OPUS optimization for x86/fixed point
May 2014

## Slide 2: Agenda
How to enable optimization
Optimization Performance comparison
Optimization level
Optimization Code list
How to verify Optimization

## Slide 3: How to enable optimization
./autogen.sh
./configure --enable-fixed-point --enable-intrinsics
NOTE:
Default optimization is disabled, which is identical to original code
ENABLE_OPTIMIZE macro defines if optimization is enabled
Optimization only for x86 platform
Optimization only for fixed point

## Slide 4: Optimization Performance comparison
OPUS | Encode time(us) | Percentage
Original | 188.945 | --
Optimization for Cisco | 128.479 | 31.7%(59.739us)
Host machine for testing:
CentOS6.3 64bit
CPU Xeon E5620 @ 2.4GHz
Physical machine
Opus parameter:
bandWidth:8KHZ
Sampling Rate:16KHZ
VBR: enable
Frame size:20ms
Complexity:2
FEC: enable
DTX: enable
Packet loss percentage:10
BitRate:35kbps
Channel: mono

## Slide 5: Optimization Level
Pure C + 64-bit multiplication + inline assembly
SSE2 + Pure C + 64-bit multiplication + inline assembly
SSE4.2 + Pure C + 64-bit multiplication + inline assembly

## Slide 6: Code change list
File | Function | Level
celt/ptich.c | celt_inner_prod() | SSE2
celt/celt_lpc.c | celt_fir() | SSE4.2
silk/fixed/LP_analysis_filter_fix.c | LP_analysis_filter_fix() | Pure C
silk/fixed/burg_modified_fix.c | silk_burg_modified() | SSE4.2
silk/VAD.c | silk_VAD_GetSA_Q8() | SSE4.2
silk/NSQ_del_dec.c | silk_NSQ_del_dec() | SSE4.2
silk/NSQ.c | silk_NSQ() | SSE4.2
silk/NLSF_del_dec_quant.c | silk_NLSF_del_dec() | Pure C
silk/A2NLSF.c | silk_A2NLSF_eval_poly() | Pure C
silk/VQ_WMat_EC.c | silk_VQ_WMat_EC() | SSE4.2

## Slide 7: Code change list
NEW File | Function | Level
celt/x86/ptich_sse.c | celt_inner_prod_sse() | SSE2
celt/x86/celt_lpc_sse.c | celt_fir_sse() | SSE4.2
silk/fixed/x86/burg_modified_fix_sse.c | silk_burg_modified_sse() | SSE4.2
silk/x86/VAD_sse.c | silk_VAD_GetSA_Q8_sse() | SSE4.2
silk/x86/NSQ_del_dec_sse.c | silk_NSQ_del_dec_sse() | SSE4.2
silk/x86/NSQ_sse.c | silk_NSQ_sse() | SSE4.2
silk/x86/VQ_WMat_EC_sse.c | silk_VQ_WMat_EC_sse() | SSE4.2
src/opus_cpu.c | See the notes | --
src/opus_cpu.c:
Add some new functions for dynamically detecting CPU features (no SIMD, SSE2, SSE4.2), use function pointer to implement.

## Slide 8: About dynamically checking CPU type
Detect CPU type in opus_encoder_init
initialize function vectors according to CPU type
  default points to original C implementations
  points to SSE2/SSE4.2 implementations if supported

## Slide 9: How to verify optimization
Check the encoded bit-stream
  should be exactly same with original code
2. All test pass by OPUS official test:
test log:
3. Use PESQ:
Keep the same MOS value before and after optimization